## Slide 1: xBGAS: A Bridge Proposal for RV128 and HPC
John Leidel1, David Donofrio2, Farzad Fatollahi-Fard2, Kurt Keville3
1Tactical Computing Labs
2Lawrence Berkeley National Lab
3MIT

## Slide 2: Data Center Scale Addressing
Extended Base Global Address Space (xBGAS)
Goals:
  Provide extended addressing capabilities without ruining the base ABI
    EG, RV64 apps will still execute without an issue
  Extended addressing must be flexible enough to support multiple target application spaces/system architectures
    Traditional data centers, clouds, HPC, etc..
  Extended addressing must not specifically rely upon any one virtual memory mechanism
    EG, provide for object-based memory resolution
What is xBGAS NOT?
  …a direct replacement for RV128

## Slide 3: Application Domains
HPA-FLAT
  High performance analytics flat addressing
  For extremely large datasets that are too difficult/time consuming to shard
MMAP-IO
  Map storage tiers into address space
  Potential for object-based addressing
  See DDN WOS
Cloud-BSP
  Potential for global object visibility for in-memory cloud infrastructures (Spark)
  Reduce the time/cost to port Java to a full 128-bit addressing model
HPC-PGAS
  High Performance Computing: Partitioned Global Address Space

## Slide 4: HPC-PGAS
Traditional message passing paradigm has tremendous amount of overhead
  User library overhead, driver overhead
  Optimized for large data transfers
  Management of communication for Exascale-class systems
We have excellent examples of low-latency PGAS runtimes, but little hardware/uArch support
  LBNL: GASnet
  PNNL: Global Arrays/ARMCI
  Cray: Chapel
  OpenSHMEM
Part 0
Part 1
Part 2
Part 3
Part 4
get
get
get
put
put
put

## Slide 5: Addressing Architecture
uArch maps extended addressing into RV64
  We hope to generalize this for RV32 as well
CSR bits encoded to appear as standard RV64 uArch
  XLEN maps to RV64
  TBD whether we need additional interrupts and exceptions
Addition of extended {eN} registers that map to base general registers
Extended registers are manually utilized via extended load/store/move instructions

## Slide 6: ISA Extension
Instructions are split into three blocks:
  Base integer load/store
  Raw integer load/store
  Address management
Base integer load/store (I-type)
  Permits loading/storing all base RV64I data types using standard mnemonic
  EX: eld rd, imm(rs1)
  The extended register mapped to the same index as ’rs1’ is implied
Raw integer load/store (R-type)
  Permits loading/storing using explicit extended registers combined with explicit base registers (no imm)
  erld rd, rs1, ext2
  LOAD( ext2[127-64], rs1[63-0] )
Address Management
  Permits explicit manipulation of the extended register contents
  eaddie extd, rs1, imm
  extd = rs1+imm

## Slide 7: ISA Extension Encodings
Base Integer Load/Store
Raw Integer Load/Store
Address Management
Assembly Mnemonics

## Slide 8: ABI (Calling Convention)
This is where things get tricky…
The base RV{32,64} ABI defines:
  Context save/restore space
  Call/return register utilization
  Caller/Callee saved state
  Core data types
We want to preserve as much as possible while providing extended addressing
Many outstanding questions
  How do we link base RV objects with objects containing extended addressing?
  How do we address the caller/callee saved state with extended registers?
  Debugging and debugging metadata?

## Slide 9: Research & Progress
Software
  Data Intensive Scalable Computing Lab at Texas Tech is leading the software research
  Current xBGAS spec implemented in LLVM compiler
  Study the various application domains
Hardware
  TCL/LBNL/MIT leading hardware effort
  Exploring pipelined and accelerator-based implementations
Other Topics
  Operating system (context save info)
  Debugging
  Programming Model

## Slide 10: Community Support & Interest
xBGAS spec available on Github
  https://github.com/tactcomplabs/xbgas-archspec
RISC-V Tools Branch from Priv-1.9 in progress
  https://github.com/tactcomplabs/riscv-tools
We welcome comments/collaborators!

## Slide 11: Acknowledgements
Farzad Fatollahi-Fard, David Donofrio, John Shalf: Lawrence Berkeley Lab
Kurt Keville: MIT
Xi Wang, Frank Conlon, Yong Chen: Texas Tech University
Bruce Jacob: University of Maryland
Steve Wallach: Micron